## Slide 1: IoT Practice-I Firmware Programming of ATmega328

## Slide 2: Objective
Understanding the basics of hardware structure and its operations of 8-bit microprocessor.
How to program the application software (firmware) executed on 8-bit microprocessor.

## Slide 3: Training Kit
KT IoTMakers Starter Kit
  Arduino UNO compatible
    http://www.wowsystem.co.kr/index.php
Main board
  Processor : ATmega328-AU,
    https://kr.mouser.com/ProductDetail/Microchip-Technology-Atmel/ATMEGA328-AU?qs=lwdSMh1%2FoYJRHuGBjWz9Pg==
I/O board
  Wi-Fi Shield
  LED Module
  FND Module
  Ambient Light Sensor Module
  Temperature Sensor Module
  Ultrasonic Sensor Module
  Motor Module

## Slide 4: Practice Environment
Program development environment
  Integrated Development Environment (IDE)
    Atmel Studio 7 (atmel.com)
    Arduino Software (Arduino.cc)
    3rd-party tools, ….
Reference materials
  ATmega328 Datasheet
  AVR Instruction Set Manual

## Slide 5: ATmega328 Processor
A low-power CMOS 8-bit microcontroller based on ARV RISC core
  131 instructions : most single clock cycle execution
  32 x 8 general purpose registers
  ~ 20MIPS @ 20MHz
  On-chip 2-cycle multiplier
  Memory : Flash/EEPROM/RAM
    Write/Erase cycles : 10K Flash/100K EEPROM

## Slide 6: ATmega328 Processor
Peripherals
  23 I/O lines
  2 x 8-bit timer/counter
  1 x 16-bit timer/counter
  RTC
  6 PWM channels
  8-ch 10-bit ADC in TQFP/MLF/QFN package
  6-ch 10-bit ADC in PDIP package
  1 UART
  1 SPI
  1 I2C
  Watchdog timer
  Analog comparator
Operating condition
  Power supply : 1.8~5.5V
  Temperature : -40~85 degree
  Speed grade : 0~4MHz@1.8~5.5V, 0~10MHz@2.7~5.5V, 0~20MHz@4.5~5.5V
  Power consumption : 0.2mA@active, 0.1uA@power-down, 0.75uA@power-save

## Slide 7: ATmega328 Processor
Block diagram of ATmega328

## Slide 8: AVR Core

## Slide 9: Overview of AVR Core
AVR Core
  CPU core of ATmel processor
    8-bit RISC micro-controller
    A modified Harvard architecture : separate I/D memory.
History of AVR
  In 1996, 2 students(Alf-Egil Bogen, Vegard Wollan) in Norweign Institute of Technology (NTH) originally designed a uRISC processor.
  In 2016.1, Microchip acquired ATmel for $3.56 billion.
    Microchip provides PIC & AVR processor.
Line-up of AVR processors
  https://www.microchip.com/design-centers/8-bit

## Slide 10: Block Diagram of AVR Core
Program
Memory
Control
Unit
Data
Memory
I/O
Registers

## Slide 11: Pipelining of AVR Core
2-stage pipeline
  1 instruction cycle consists of 2 operation cycles.
  2 operation cycles are overlapped.
    During one instruction is executed, the next one is pre-fetched from program memory.
      Instruction pre-fetch
I-Fetch
I-Execute
I-Fetch
I-Execute
I-Fetch
I-Execute
Sequential Execution of a series of Instructions
2-Stage Pipelining
I-Fetch
I-Execute
I-Fetch
I-Execute
I-Fetch
I-Execute
Pipeline
Latency
Concurrent Execution
I-Fetch
I-Execute
Instruction Cycle
Operation Cycle

## Slide 12: Instruction Execution Timing
Parallel instruction fetches & instruction executions
Single cycle ALU operation

## Slide 13: Memory Structure of AVR Core
Harvard Architecture
  Separate program memory & data memory
    Separated access bus.
    Parallel memory access is possible, so good for pipelining.
CPU
Program
Memory
Data
Memory
CPU
Program
Memory
Data
Memory
Simultaneous code & data access is not possible.
Parallel code & data access is possible.
Von Neumann Structure
Harvard Structure

## Slide 14: Registers of AVR Core
General Purpose Register (GPR)
Status Register (SREG)
Stack Pointer (SP)
Address Pointer Register (X-, Y-, Z-Register)

## Slide 15: General Purpose Register (GPR)
32 x 8-bit register
  R0~R31
    R26~R31 are used as address pointer registers.
  32 GPR’s are mapped into data memory space(0x00 ~ 0x1F).
    Memory access instruction can access to GPR’s.

## Slide 16: Status Register (SREG)
Contains information about the result of the most recently executed arithmetic instruction.
  Used for altering program flow in order to perform conditional operations
SREG is also mapped to data memory(0x5F).
Bit configuration of SREG
  I : Global interrupt enable, 1 = enabled
  S : Sign bit, S = N XOR V
  V : 2’s complement overflow flag
  N : Negative flag, Z : zero flag, C : carry flag
  H : Half carry flag
  T : Temporal storage for bit copy instruction(BLD, BST)

## Slide 17: Stack
Stack
  Data memory space specially reserved for
    storing temporal data, passing parameters, local variables, return address, used-registers-saving when function call, interrupt request are processed.
  Special instructions are used to handle stack : PUSH, POP
  Types of stack
    Ascending/Descending
    Full/Empty
    hardware stack : stack in registers
POP
high
low
PUSH
SP

## Slide 18: Stack Pointer (SP)
Point to the top of stack
Stack pointer in AVR core
  16-bit stack pointer
    2 x 8-bit registers (SPH, SPL) are connected to make 16-bit stack pointer.
  SPH, SPL : I/O space of data memory at 0x5D, 0x5E.
  When processor is reset, SP is automatically set to ‘0’.
    Before interrupt or function call is issued, SP should set to be over 0x60.
      GPR & I/O space of data memory : 0x00~0x60.
Stack operations
  PUSH : write data to stack, SP is decreased.
  POP : read data from stack, SP is increased.

## Slide 19: Address Pointer Register
AVR core has 3 address pointer registers(X, Y, Z)
  16-bit pointer
    2 x 8-bit GPR’s are connected.
  To access data memory indirectly, 16-bit address pointer register is used.
X-Register
  R26(low-byte), R27(high-byte)
Y-Register
  R28(low-byte), R29(high-byte)
Z-Register
  R30(low-byte), R31(high-byte)
  Used when a constant stored in program memory is accessed using LPM, ELPM, SPM instructions.

## Slide 20: On-chip Memory of AVR Core
Program memory
  Flash memory to store program code.
  Non-volatile
  Mostly read-only.
Data memory
  SRAM
    Temporal storage for data(variable, constant) used during program execution.
    Volatile
    Read & Write
  EEPROM
    Permanent storage for data
    Non-volatile
    Mostly read-only.

## Slide 21: Program Memory
Configuration of flash memory
  32K/64K/128K x 2-bytes 구성
    Instruction length : 2-bytes, 4-bytes
  Program counter : 15/16/17-bit
Support to store data in program memory for the use of constant & lookup table.
How to write binary code(executable) to flash memory (fusing)
  SPI, JTAG interface.
  Duration : 10,000 write/erase cycles

## Slide 22: Program Memory
Program memory is divided into 2 sections.
  Boot program section
    Store boot program or the program supporting self-programming function.
  Application program section
    Store application program.
The size of each section is adjustable (configurable).
Lock bit is used to protect any unwanted write to each section.

## Slide 23: Data Memory
SRAM data memory
Unified data memory map
  GPR, I/O registers, internal data SRAM are mapped to an unified memory space.
Addressing modes
  Direct, Indirect, Indirect with displacement, Indirect with pre-decrement, Indirect with post-increment.
How to access to I/O space
  Same as data memory access : LD/LDS/LDD, ST/STS/STD instructions.
  Access as a separate I/O space : IN/OUT instructions.

## Slide 24: I/O Space
I/O Registers within the address range 0x00 - 0x1F are directly bit-accessible using the SBI and CBI instructions.
Special Function Registers (SFR)
  SREG : $5F
  SP : SPH ($5E), SPL ($5D)

## Slide 25: Data Memory
Memory Access : 2 cycles

## Slide 26: Data Memory (EEPROM)
On-chip EEPROM
  Permanent data storage. Non-volatile
    Separate memory space.
  Duration
    100,000 write/erase cycle.
EEPROM access registers
  used for EEPROM access.
    EEPROM address register : EEARH, EEARL
    EEPROM data register : EEDR
    EEPROM control register : EECR
CPU halt
  When the EEPROM is read, the CPU is halted for four clock cycles before the next instruction is executed.
  When the EEPROM is written, the CPU is halted for two clock cycles before the next instruction is executed.
Notes: AVR 코어에는 4 KB 크기의 EEPROM 메모리가 내장되어 있다. 이 메모리는 비휘발성 (non-volatile) 메모리이기 때문에 전원공급이 중단된 경우에도 저장된 데이터를 유지할 수 있기 때문에 데이터 보관용으로 사용될 수 있다. 즉, 일반 컴퓨터의 하드 디스크 역할을 한다. SRAM 은 전원공급이 중단되면 데이터가 사라지기 때문에 데이터 보관이 필요한 경우, EEPROM 으로 저장하여 보관하고 다시 사용할 경우에는 EEPROM 에서 직접 읽어서 사용하거나, SRAM 으로 복사한 후 사용할 수 있다. EEPROM 에서 직접 읽는 경우는 시간이 많이 걸리기 때문에, SRAM 으로 복사한 후 사용하는 것이 프로그램의 실행속도 향상에 좋다.
EEPROM 은 디바이스 특성상 읽고 쓰는 횟수에 제한이 있다. AVR 코어에는 10 만번 정도를 읽고 쓸 수 있는 EEPROM 을 내장하고 있다.
EEPROM 은 데이터 메모리 공간과 별도의 어드레스 공간을 가지고 있다. 따라서, 별도의 메모리 인터페이스를 사용하기 위하여 전용 레지스터를 사용한다. 메모리를 사용하기 위해서는 어드레스, 데이터, 컨트롤 신호가 필요하기 때문에 EEPROM 메모리를 액세스하기 위한 전용 어드레스 레지스터 (EEAR : EEPROM Address Register), 데이터 레지스터(EEDR : EEPROM Data Register), 컨트롤 레지스터 (EECR : EEPROM Control Register) 를 가지고 있다.
4KB 크기의 EEPROM 공간을 사용하기 위해서는 12-비트 어드레스가 필요하다. 따라서, 8-비트 레지스터 2개를 연결해서 사용한다. 즉, 12-비트 어드레스의 상위 바이트를 저장하는 EEARH 와 하위 바이트를 저장하는 EEARL 2 개를 연결해서 사용한다.
EEPROM 을 읽거나 쓰는 시간이 CPU 클럭 싸이클 시간보다 길기 때문에 CPU 는 EEPROM 액세스가 완료될 때까지 기다려야 한다. EEPROM 을 읽을 경우에는 4 클럭 싸이클, 쓸 때에는 2 클럭 싸이클 동안 CPU 가 동작을 중지한다.

## Slide 27: I/O’s of ATmega328

## Slide 28: On-chip I/O’s
GPIO (General purpose I/O)
  23 x Programmable I/O’s
    8-bit port :B, D
    7-bit port : C
Timer
  2 x 8-bit timer (Timer-0/Timer-2)
  1 x 16-bit timer (Timer-1)
  1 x RTC(realtime clock) with separate osclliator
  1 x Watchdog timer : programmable
PWM (Pulse Width Modulation)
  6 x PWM channels

## Slide 29: On-chip I/O’s
Analog interface
  8-ch 10-bit ADC in TQFP/MLF/QFN package
  6-ch 10-bit ADC in PDIP package
  Analog comparator
Communication interface
  1 x UART
  1 x SPI
  1 x I2C

## Slide 30: GPIO

## Slide 31: GPIO
General Purpose I/O
  Multi-purpose digital input/output pin
  Voltage level : TTL-level
    If logical ‘1’ is out to GPIO, the voltage level corresponding to logical value ‘1’ (ex, 5V) is sustained.
ATmega328의 GPIO
  23 pins are available for GPIO.
    8-bit port :B, D
    7-bit port : C
  Alternate function

## Slide 32: GPIO Control Registers
GPIO control registers control the operations of GPIO.
Data direction register (DDR)
  Control the flow direction of GPIO. R/W
    ‘0’ as input, ‘1’ as output
    Read/Writable
Input Pins Address (PIN)
  Store the input value of GPIO pin.
    Read/Writable
Data register (PORT)
  Output register.
        Read/Writable
If you want to send data to GPIO, just write data value to PORT register. If you get data from GPIO, read PIN register.

## Slide 33: Block Diagram of GPIO
Data Register (PORT)
Port Input Pin (PIN)
Data Direction Register (DDR)

## Slide 34: GPIO Control of Port B

## Slide 35: GPIO Control
GPIO control register map of AVR series
Port | DDR | PORT | PIN
A | 0x21 | 0x22 | 0x20
B | 0x24 | 0x25 | 0x23
C | 0x27 | 0x28 | 0x26
D | 0x2A | 0x2B | 0x29
E | 0x2D | 0x2E | 0x2C
F | 0x30 | 0x31 | 0x2F
G | 0x33 |  | 
H | 0x101 | 0x102 | 0x100
J | 0x104 | 0x105 | 0x103
K |  |  | 
L |  |  | 

## Slide 36: Alternate Function 사용

## Slide 37: Alternate Port Function
Port-B

## Slide 38: Alternate Port Function
Port-C

## Slide 39: Alternate Port Function
Port-D

## Slide 40: GPIO Pull-up Resistor
To protect an input pin in float state, a pull-up/down resistor is used.
GPIO in AVR, has an internal pull-up register (min.=20, max.=50Kohm)
  input mode에서 사용
    After setting GPIO to input mode, writing ‘1’ to GPIO will internally connect pull-up resistor to input pin.
    If pull-up resistor is not necessary, writing ‘0’ to GPIO or changing its pin mode to output is required.
  To disable all pull-up resistors of all GPIO’s, set PUD bit(flag) of MCUCR to ‘1’.
pull-up resistor

## Slide 41: GPIO Pull-up Resistor
Internal pull-up register

## Slide 42: Electrical Characteristics of GPIO

## Slide 43: Electrical Characteristics

## Slide 44: GPIO Pin Macro
header file : ~Arduino/hardware/tools/avr/avr/include/avr/iomxx0_1.h
#include<avr/io.h>
#include<util/delay.h>
int main(){
char i;
unsigned char LED_Data = 0x00;
DDRE = 0xFF; // Port E = output
while(1){
PORTE = LED_Data;
LED_Data++;
for(i=0;i<10;i++)
_delay_ms(100);
}
return 0;
}
#include<avr/io.h>
int main(){
DDRE = 0xFF; // Port E = output
DDRB = 0x00; // Port B = input
while(1){
PORTE = PINB; // push & display
}
return 0;
}
pinMode()
digitalWrite()
pinMode()
digitalWrite()
digitalRead()

## Slide 45: Interrupt

## Slide 46: Overview of Interrupt
Polling vs. Interrupt ???
A good way to interact between I/O device and CPU.
  CPU request a task to I/O device.
  After I/O device finished the task given by CPU, it activates interrupt request signal to acknowledge its finish to CPU.
Interrupt source
  Internal interrupt : interrupt generated by abnormal situation during program execution.
    Trap : divided by zero, memory access violation
    Software interrupt : execution of SWI instruction.
  External interrupt : hardware interrupt generated by internal/external I/O device.

## Slide 47: Overview of Interrupt
Interrupt mask
  A bit which controls whether an interrupt can be processed(enabled) or not(disabled).
    NMI (Non-Maskable Interrupt) : reset
  Global mask : applied to all interrupts
  Local mask : applied to a specific interrupt.
Interrupt detection
  Polled interrupt checking : periodical check the interrupt request(flag).
  Vectored Interrupt checking : if interrupt is requested, the flow of program execution branches automatically to a specific address of program memory.
Interrupt Service Routine (ISR)
  Interrupt handling function.
    Interrupt handler.

## Slide 48: Overview of Interrupt
Interrupt vector
  A pre-defined address to which the flow of program execution branches whenever interrupt is requested.
    The start address of ISR
Interrupt vector table(IVT)
  A table of interrupt vectors (pointers to ISR)
  The table that specifies the addresses of all interrupt handlers.
Interrupt Priority
  Urgency level of each interrupt.
    In general, Lower priority means higher urgency.
  Used to decide the order of interrupt handling when multiple interrupts are requested at the same time, or new interrupt is requested during the previous interrupt is handled.

## Slide 49: Interrupt Sources of ATmega328
26 x interrupt sources
The lower the address the higher is the priority level.

## Slide 50: Interrupt Masking of ATmega328
Interrupt masking
  In order to allow interrupt, global, local interrupt mask should be enabled.
  Global interrupt mask
    SREG의 I-bit : 1(enable), all interrupts are enabled.
    Whenever entering ISR, I-bit is automatically set to ‘0’(disable), and set to ‘1’ after return from ISR.
  Private interrupt mask
    Determines whether each interrupt is enable or not.
To enable an interrupt request, both global & local mask should be set to ‘1’.

## Slide 51: External Interrupt of ATmega328
External interrupt
  Triggered by INT0, 1 pin or any of PCINT0~23(pin change interrupt).
    PCI0 will trigger if any enabled PCINT[7:0] pin toggles.
    PCI1 will trigger if any enabled PCINT[14:8] pin toggles.
    PCI2 will trigger if any enabled PCINT[23:16] pin toggles.
Interrupt detection
  External interrupts can be triggered by a falling/rising edge, low level.
  Depends on the setting of External Interrupt Control Register(EICR).
Even if INT, PCINT are configured as output, interrupt will trigger.
  Provides a way of generating a software interrupt.

## Slide 52: Control Register of External Interrupt
External interrupt
  EICRA : external interrupt control register
  EIMSK : external interrupt mask register
  EIFR : external interrupt flag register
Pin change interrupt (PCI)
  PCICR : PCI control register
  PCMSK2, 1, 0 : PCI mask register
  PCIFR : PCI flag register

## Slide 53: Mask of External Interrupt
EIMSK(External Interrupt Mask Register)
  External interrupt mask register
    0 (disable), 1 (enable)
    When the INTx bit is set (one) and the I-bit in the Status Register (SREG) is set (one), the external pin interrupt is enabled.

## Slide 54: Flag of External Interrupt
EIFR (External Interrupt Flag Register)
  When an edge or logic change on the INTx pin triggers an interrupt request, INTFx becomes set (one).
  If the I-bit in SREG and the INTx bit in EIMSK are set (one), the MCU will jump to the corresponding Interrupt Vector.
  The flag is cleared when the interrupt routine is executed.
  Alternatively, the flag can be cleared by writing a logical one to it.
  This flag is always cleared when INTx is configured as a level interrupt.

## Slide 55: Sense Control of External Interrupt
The sensing way of external interrupted is controlled by ISC(interrupt sense control) field of EICRA.
ISC field : ISC[1:0]

## Slide 56: Sense Control of External Interrupt
Minimum pulse width
  If edge or toggle interrupt is selected, pulses that last longer than one clock period will generate an interrupt.
  If low level interrupt is selected, the low level must be held until the completion of the currently executing instruction to generate an interrupt.

## Slide 57: Control of Pin Change Interrupt
PCI Control Register
  PCI enable flag (PCIE2,1,0)
    PCIE = 1 (enable)
When the PCIEx bit is set (one) and the I-bit in the Status Register (SREG) is set (one), pin change interrupt is enabled.
Any change on any enabled PCINT[23:0] pin will cause an interrupt.
  PCIE0 : PCINT[7:0]
  PCIE1 : PCINT[15:8]
  PCIE2 : PCINT[23:16]

## Slide 58: Control of Pin Change Interrupt
PCI mask register
PCI flag register

## Slide 59: ISR Programming
#include <io.h>
#include <interrupt.h>
// INT0 interrupt service routine
ISR(SIG_INTERRUPT0) // SIGNAL(SIG_INTERRUPT0)
{
  // body
}
int main(void)
{
DDRD = 0xFE; // interrupt source = D port
EIMSK = 0x01; // enable INT-0
sei(); // enable global interrupt
for (;;) ; // main body
}
sei() : global interrupt enable,
cli() : global interrupt disable
ISR for external interrupt (INT0)

## Slide 60: Example
#include<avr/io.h>
#include<avr/interrupt.h>
#include<util/delay.h>
unsigned char Time_STOP = 0;
SIGNAL(SIG_INTERRUPT0);
int main(){
unsigned char LED_Data = 0x01;
DDRD = 0xFE; // Port D.0  Switch (INT0)
DDRE = 0xFF; // Port E  LED
EICRA = 0x0F; // Detect policy of INT0, INT1  rising edge
EICRB = 0x00; // others  low level
EIMSK = 0x01; // Mask of INT0  enable
EIFR = 0x01; // Flag of INT0  clear
sei(); // global interrupt mask -> enable
while(1) {
PORTE = LED_Data;
if(Time_STOP == 0) {
if(LED_Data == 0x80) LED_Data = 0x01;
else LED_Data <<= 1;
}
_delay_ms(100);
}
return 0;
}

## Slide 61: Example
ISR(SIG_INTERRUPT0) { // ISR of INT0
cli();
if(Time_STOP == 0)
Time_STOP = 1;
else
Time_STOP = 0;
sei();
}

## Slide 62: Arduino ISR
Interrupt pin
  Digital pin : 2(INT0), 3(INT1) in Uno
Functions for interrupt handling
  Registration of ISR : “attachInterrupt()”
    Options of interrupt sensing method
      FALLING, RISING, CHANGE, LOW
  Mapping digital pin to interrupt number : “digitalPinToInterrupt()”
  ISR removal : “detachInterrupt()”
  Interrupt enabling/disabling : “interrupts()/nointerrupts()”
  ISR : no parameters, no return
    Use global variable for data exchange.
attachInterrupt(interrupt, ISR, mode);
* interrupt : interrupt 번호.
* ISR : interrupt service routine,
* mode : interrupt sensing method
attachInterrupt(digitalPinToInterrupt(pin), ISR, mode);

## Slide 63: Arduino ISR
Example
int pin = 13; volatile int state = LOW; void setup() { pinMode(pin, OUTPUT); attachInterrupt(digitalPinToInterrupt(pin), blink, CHANGE); } void loop() { digitalWrite(pin, state); } void blink() { state = !state; }

## Slide 64: Changing the Location of IVT
Moving IVT to boot section using IVSEL, IVCE.
IVSEL(interrupt vector select) bit of MCUCR
  When the IVSEL bit is cleared (zero), the Interrupt Vectors are placed at the start of the Flash memory.
  When this bit is set (one), the Interrupt Vectors are moved to the beginning of the Boot Loader section of the Flash.
  The actual address of the start of the Boot Flash Section is determined by the BOOTSZ Fuses.
IVCE(interrupt vector change enable) bit of MCUCR
  To avoid unintentional changes of Interrupt Vector tables, a special write procedure must be followed to change the IVSEL bit:
    1. Write the Interrupt Vector Change Enable (IVCE) bit to one.
    2. Within four cycles, write the desired value to IVSEL while writing a zero to IVCE.
void Move_interrupts(void)
{
/* Enable change of Interrupt Vectors */
MCUCR = (1<<IVCE);
/* Move interrupts to Boot Flash section */
MCUCR = (1<<IVSEL);
}

## Slide 65: Changing the Location of Reset Vector
Changing reset vector using BOOTRST fuse bit.
Reset Vector can also be moved to the start of the Boot Flash section by programming the BOOTRST Fuse.
Fuse bit : 1 (unprogrammed), 0 (programmed)

## Slide 66: Changing the Size of Boot Section.
The size of boot section is configured by BOOTSZ[1:0] fuse bits.
The Actual address of the start of the Boot Flash Section is determined by the BOOTSZ Fuses.

## Slide 67: Read-While-Write Self-Programming
Boot Loader Support feature of ATmega328 provides a real Read-While-Write Self-Programming mechanism for downloading and uploading program code by the MCU itself.
  Allows flexible application software updates controlled by the MCU using a Flash-resident Boot Loader program.
  Boot Loader program can use any available data interface and associated protocol to read code and write (program) that code into the Flash memory, or read the code from the program memory.
  The program code within the Boot Loader section has the capability to write into the entire Flash, including the Boot Loader memory.
  The Boot Loader can thus even modify itself, and it can also erase itself from the code if the feature is not needed anymore.

## Slide 68: Read-While-Write Self-Programming
Additionally, flash memory is divided into two fixed section.
  Read-While-Write (RWW) section
    When erasing or writing a page located inside the RWW section, the NRWW section can be read during the operation.
    If a Boot Loader software update is programming a page inside the RWW section, it is possible to read code only from NRWW section of the Flash.
  No Read-While-Write (NRWW) section :
    When erasing or writing a page located inside the NRWW section, the CPU is halted during the entire operation.
    The code located in the NRWW section can be read when the Boot Loader software is updating a page in the RWW section.
    When the Boot Loader code updates the NRWW section, the CPU is halted during the entire Page Erase or Page Write operation.

## Slide 69: Read-While-Write Self-Programming
Configuration of RWW/NRWW according to BOOTSZ[1:0] fuses
Fuse bit : 1 (unprogrammed), 0 (programmed)

## Slide 70: Read-While-Write Self-Programming
Configuration of RWW/NRWW according to BOOTSZ[1:0] fuses
Fuse bit : 1 (unprogrammed), 0 (programmed)

## Slide 71: Read-While-Write Self-Programming
RWW/NRWW of ATmega328

## Slide 72: Timer

## Slide 73: Overview
Timer
  General purpose H/W counter
    Time measurement
    Counting the frequency of event occurrence.
    Waveform generation (PWM)
      control the power of supplying to external device.
Basic structure of timer in AVR core
    PWM : Pulse Width Modulation
    TCNT : Timer/Counter
    OCR : Output Compare match Register
    ICR : Input Capture Register
    TOV : Timer OVerflow
    OCF : Output Compare Flag
    ICF : Input Capture Flag
TCNT
CLK_I/O/Tn/TOSC
=
OCF
Waveform Generator
Waveform (PWM)
prescaler
TOV
OCR
ICR
ICF

## Slide 74: Timer of ATmega328
3 Timers
  2 x 8-bit timer : Timer-0, 2
  1 x 16-bit timer : Timer-1
Operation mode
  Normal mode
  CTC(Clear Timer on Compare Match) mode
  Fast PWM mode
  Phase correct PWM mode
  Phase and Frequency Correct PWM mode
    16-bit timer only
Timer interrupt
  TOV (timer overflow)
    When the value of timer is changed from 0xFF to 0x00.
  OCF (output compare match flag)
    When the value of timer is same as that of OCR.
  ICF (input capture flag)
    When the value of timer is captured into ICR.

## Slide 75: Block Diagram of Timer-0
8-bit timer

## Slide 76: Block Diagram of Timer-1
16-bit timer

## Slide 77: Block Diagram of Timer-2

## Slide 78: Operation Mode
Operation mode
  According to operation mode, counting sequence of counter is different..
    Normal mode
    CTC(Clear Timer on Compare Match) mode
    Fast PWM mode
    Phase correct PWM mode
    Phase and Frequency Correct PWM mode
      16-bit timer only
Configuration of operation mode
  WGM and COM field of TCCR
    WGM : determine counting sequence.
    COM : control OC output on compare matched.
      PWM mode : inverted or non-inverted
      Non-PWM mode : clear, set, toggle
    PWM : Pulse Width Modulation
    CTC : Clear Timer on Compare match
    WGM : Waveform Generation Mode
    COM : Compare Output Mode
    TCCR : Timer/Counter Control Register
    OC : Output Compare

## Slide 79: Normal Mode
Single-slope operation
  Always up counting
  BOTTOM(0x00)  MAX (0xFF)
  No initialization
TOV is set when TCNT becomes 0x00 from 0xFF.
Preset of TCNT is possible.

## Slide 80: CTC Mode
CTC (Clear Timer on Compare match) mode
Single-slope operation
  BOTTOM  TOP (OCR0A)
Whenever TCNT equals to OCR
  Timer set to ‘0’, OCF interrupt is generated, OC pin toggle.
F(OC) = f_CLK_I/O / (2*N*(1+OCR),
  N (prescale factor)=1, 8, 64, 256, 1024

## Slide 81: Fast PWM Mode
Single-slope operation
  BOTTOM  TOP : 0xFF(WGM=3), OCR0A(WGM=7)
Whenever TCNT equals to TOP
  TOV or OCF is generated.
Whenever TCNT equals to OCR
  Non-inverting PWM mode : OCF is generated, OC becomes ‘0’, and if BOTTOM, change to ‘1’.
  Inverting PWM mode : reverse of non-inverting mode.
F(OC) = f_CLK_I/O / (N*256), N=1, 8, 64, 256, 1024

## Slide 82: Phase Correct PWM Mode
Dual-slope operation
  BOTTOM  TOP  BOTTOM (up/down counting)
  TOP : 0xFF (WGM[2:0]=1), OCR0A (WGM[2:0]=5)
TCNT=OCR
  OCF is generated.
  In non-inverting mode & up-counting, OC becomes to ‘0’. If down-counting, OC becomes to ‘1’.
TCNT=BOTTOM : TOV is generated.
TCNT=TOP : OCR value is updated.
F(OC) = f_CLK_I/O / (N*510), N=1, 8, 64, 256, 1024

## Slide 83: Phase & Frequency Correct PWM Mode
Dual-slope operation
  BOTTOM  TOP  BOTTOM
  TOP : ICR (WGM=8), OCR (WGM=9)
TCNT=OCR
  OCF is generated.
  If non-inverting mode & up-counting, OC = ‘0’, and if down-counting, OC=‘1’.
TCNT=BOTTOM
  TOV is generated.
  OCR/TOP value is updated.
TCNT=TOP
  If TOP is configured by
    OCR, OCF is generated.
    ICR, ICF is generated.
F(OC) = f(CLKI/O) / (2*N*TOP)

## Slide 84: Timer Registers
TCNT : Timer/Counter Register
  Store counter value.
TCCR : Timer/Counter Control Register
  Control the operation of timer
TIMSK : Timer/Counter Interrupt Mask Register
  Enable/disable interrupt of timer
TIFR : Timer/Counter Interrupt Flag Register
  Interrupt flags
OCR : Output Compare Register
  The value compared with TCNT
ICR : Input Capture Register
  The captured value of TCNT
ASSR (Asynchronous Status Register)
  Control of external clock
GTCCR (General Timer/Counter Control Register)
  Control of prescaler reset.

## Slide 85: TCNT
Timer/counter register itself
  Stores counter’s present value.
  TCNT0,2 : 8-bit
  TCNT1 : 16-bit, TCNTnH + TCNTnL 연결사용
Timer-2
Timer-0

## Slide 86: TCNT
Timer-1

## Slide 87: TCCR
Timer control register
  Control of timer’s clock, operation mode, output of OC pin, input of ICP.
    CS (Clock Select) field : select clock source.
    WGM (Waveform Generation Mode) field : select operation mode.
    COM (Compare Output Mode) field : control the output of OC pin.
    FOC (force output compare) field : control the output of OC pin.
    ICNC (input capture noise canceler) flag : control the input of ICP pin.
    ICES (input capture edge select) flag : control the input of ICP.
  Timer-0,2 : TCCRnA, TCCRnB, n=0,2
  Timer-1 : TCCRnA, TCCRnB, TCCRnC, n=1

## Slide 88: TCCR
Timer-0,2
Timer-1

## Slide 89: TCCR
WGM (waveform generation mode) field
Timer-0,2

## Slide 90: TCCR
WGM (waveform generation mode) field
Timer-1

## Slide 91: TCCR
COM (compare output mode) field
Timer-0, 2

## Slide 92: TCCR
COM (compare output mode) field
Timer-0,2

## Slide 93: TCCR
COM (compare output mode) field
Timer-1

## Slide 94: TCCR
COM (compare output mode) field
Timer-1

## Slide 95: TCCR
CS (clock select) field
  Select clock source
Timer-0
Timer-2

## Slide 96: TCCR
CS (clock select) field
  Select clock source
Timer-1

## Slide 97: TCCR
FOC (Force Output Compare) field
  Only applied to non-PWM modes.
  FOC = 1
    The result of compare match is transferred to waveform generator, finally output to OC pin.
      The waveform of OC pin depends on COM field.
    No interrupt, no clear on timer.
  Timer-0,2 : FOCnA, FOCnB, n=0,2
  Timer-1 : FOCnA, FOCnB, FOCnC, n=1

## Slide 98: ICNC/ICES
ICNC (input capture noise canceler) : Timer-1,3
  1 : canceler enable
    Check 4 sequences of pulses on ICP pin.
ICES (input capture edge select) : Timer-1,3
  0 : falling edge
  1 : rising edge

## Slide 99: TIMSK
TIMSK (Timer Interrupt Mask)
  Interrupt masks for TOV, OCF, ICF (1=enable)
Timer-0,2
Timer-1

## Slide 100: TIFR
Timer Interrupt Flag Register
  Store interrupt flags(TOV, OCF, ICF) of timer.
    Cleared if ‘1’ is written.
    Automatically cleared when ISR is entered.
Timer-1
Timer-0,2

## Slide 101: OCR
OCR (output compare register)
  Store target value for comparing with timer.
  Timer-0,2 : OCRnA, OCRnB, n=0,2
  Timer-1 : OCRnA, OCRnB, OCRnC, n=1,3,4,5
    OCRnxH + OCRnxL are connected to make 16-bit, x=A,B

## Slide 102: ICR
ICR (input capture register)
  Store the captured value of timer
    ICRnH + ICRnL are connected to make 16-bit register.
    Only for Timer-1.
  How to trigger the capture.
    Triggered by ICPx pin.
    Triggered by the output of analog comparator.

## Slide 103: ASSR
ASSR (asynchronous status register)
  Only for Timer-2 when external clock is used.
EXCLK : enable the external clock.
  If EXCLK=1 : use TOSC1 pin as clock source.
AS2 (asynchronous timer)
  AS2=0 : use internal clock..
  AS2=1 : generate timer clock by connecting TOSC1,2 pin & external crystal.
    When RTC is clocked by external 32.768KHz crystal.
TCN2UB (timer counter 2 update busy)
  1 if TCNT2 is used in async. mode.
TCR2AUB/TCR2BUB (timer control register 2 update busy)
  1 if TCCR2 is used in async. mode.
OCR2AUB/OCR2BUB (output compare register 2 update busy)
  1 if OCR2 is used in async. mode.

## Slide 104: GTCCR
General Timer/Counter Control Register
  TSM : Timer/Counter Synchronization Mode
    TSM=1 : Sync. mode. Timer halt.
    TSM=0 : Timer is operated, PSRASY, PSRSYNC are automatically cleared.
  PSRSYNC : prescaler reset for synchronous timer/counter.
    PSRSYNC=1 : prescaler reset
    For timer-0,1
  PSRASY : prescaler reset timer/counter2
    PSRASY=1, prescaler reset
    For timer-2

## Slide 105: ADC

## Slide 106: Overview of ADC
ADC(analog-to-digital conversion)
  Convert the analog signal representing physical quantities to digital signal.
Basic procedure of AD conversion
  Sample & Hold
    Sample the continuous analog signal and hold its signal level for a period.
      sample. & hold time
  Quantization
    Convert the sampled signal to digital value.
      Resolution

## Slide 107: Overview of ADC
Conventional methods of ADC
  direct-conversion (flash)
  Successive-approximation
  Ramp-compare (stair-case)

## Slide 108: ATmega328 ADC
Feature of ADC
  10-bit resolution successive approximation ADC
  Conversion time : 13~260 us
  Max. sampling frequency : 15 kSPS @ max. resolution.
  Input channels
    Voltage level : 0 ~ VCC
    6 x multiplexed single-ended channels
      2 additional channels only for TGFP, GFN/MLF package.
    Temperature sensor input channel
  Accuracy
    0.5 LSB integral non-linearity
    +/- 2 LSB absolute accuracy
  Additional functions
    Left adjustment for ADC result readout
    Selectable 1.1V ADC reference voltage
    Free running & single conversion
    Interrupt on conversion complete
    Sleep mode noise canceller

## Slide 109: ADC Block Diagram

## Slide 110: Conversion Timing
ADC initialization : 25 ADC clock cycles
Normal conversion : 13 ADC clock cycles
Sample-and-Hold time
  The first conversion : 13.5 ADC clock cycles
  After 1st conversion : 1.5 ADC clock cycles

## Slide 111: Single Conversion

## Slide 112: Free-running Conversion
Continuous conversion

## Slide 113: Precision of ADC
n-bit single-ended conversion
  GND : 0
  V(ref) : 2n – 1, n=10
Quantization error
  The difference between the analog signal and the closest available digital value at each sampling instant from the A/D converter.
Absolute accuracy
  The maximum difference between the actual value and the conversed value.
  Offset error, gain error, differential error, non-linearity error.
The conversion result of ADC is stored into ADC Result Register (ADCL, ADCH).
  Single-ended signal conversion
    0~1023(0x3FF)

## Slide 114: Offset/Gain Error
Offset error
  The deviation of the first transition (0x000 to 0x001) compared to the ideal transition (at 0.5 LSB).
    Ideal value: 0 LSB.
Gain error
  The deviation of the last transition (0x3FE to 0x3FF) compared to the ideal transition (at 1.5 LSB below maximum).
    Ideal value: 0 LSB

## Slide 115: INL/DNL Error
Integral Non-linearity (INL)
  The maximum deviation of an actual transition compared to an ideal transition for any code.
    Ideal value: 0 LSB.
Differential Non-linearity (DNL)
  The maximum deviation of the actual code width (the interval between two adjacent transitions) from the ideal code width (1 LSB).
    Ideal value: 0 LSB.

## Slide 116: ADC Registers
ADMUX (ADC Multiplexer Selection Register)
ADCSRA/B (ADC Control and Status Register A/B)
ADCL/ADCH (ADC Data Register Low/High)
DIDR0/2 (Digital Input Disable Register 0/2)

## Slide 117: ADMUX
ADC Multiplexer Selection Register (ADMUX)
REFS1:0 (Reference Selection Bits)
ADLAR (ADC Left Adjust Result)
  If ‘1’, the value of conversion result is left-adjusted. (MSB side).

## Slide 118: ADMUX
MUX3:0 (Analog Channel Selection Bits)
  Select the analog input.

## Slide 119: ADCSRA
ADC Control and Status Register – A
ADEN (ADC Enable)
  1 : ADC circuit enabled
ADSC (ADC Start Conversion)
  1 : conversion start. After finish, set to ‘0’ automatically.
ADATE (ADC Auto Trigger Enable)
  1 : Start at the rising edge of trigger signal.
ADIF (ADC Interrupt Flag)
  1 : After conversion is completed, set to ‘1’. For clear, write ‘1’ to it.
ADIE (ADC Interrupt Enable)
  1 : interrupt enabled.

## Slide 120: ADCSRA
ADPS2:0 (ADC Pre-scaler Select)
  Scaling factor of ADC clock

## Slide 121: ADCSRB
ADC Control and Status Register – B
ADTS[2:0] (ADC Auto Trigger Source)

## Slide 122: DIDR
DIDR (Digital Input Disable Register)
  ADC[15:0] pin의 digital input buffer disable
  It’s possible to save power consumption if DIDR set to ‘1’ only when ADC pin is used for ADC.

## Slide 123: ADCL & ADCH
ADC Data Register (ADCL, ADCH)
  Store the conversion result.
  Only after reading ADCL, ADCH can be read.

## Slide 124: Procedure of ADC use
Select the analog input channel.
Select the reference voltage & adjustment of the result.
Select conversion mode(free-running, single)
Determine the scaling factor of ADC clock.
Enable ADC.
Start ADC : Set ADSC flag of ADCSRA register to ‘1’.
After the conversion is completed, ADC complete interrupt is generated.
  - In ISR, the conversion result stored in ADCL, ADCH can be accessed.

## Slide 125: USART

## Slide 126: Overview of Serial Communication
Serial communication
  Bit-serial communication
    After converting a byte-aligned or word-aligned data into a series of bits, send each bit one-by-one serially.
  Depending on whether clock is required or not, synchronous/asynchronous is categorized.
    If clock is used to send data, it’s sync..
  Small cost, good to long distance compare with parallel communication.
Serial Protocol
  USART(Universal Synchronous and Asynchronous serial Receiver and Transmitter)
  UART(Universal Asynchronous serial Receiver and Transmitter)
Usage
  Simple & low cost data transfer
  Status monitoring & control of various types of electrical & electronic devices.

## Slide 127: Type of Serial Communication
Type of data transfer
  Bit-serial
    Bit-wise data transfer.
    Save the transmission line cost.
    Slow transmission speed.
  Bit-parallel (byte-serial)
    Data transfer in bytes.
    High transmission line cost
    Fast transmission speed
Term-1
Term-2
Term-1
Term-2
Bit-serial
Bit-parallel

## Slide 128: Type of Serial Communication
Type of transmission path
  Simplex : only one way
  Half-duplex : both way, but one way at a time.
  Full-duplex : both way at the same time
Simplex
Half-duplex
Full-duplex

## Slide 129: Type of Serial Communication
Type of Signaling
  Balanced : 2-wire(+, -) transmission.
    Strong to noise (high noise immunity).
    Good for long distance transmission.
    High cost
  Unbalanced : 1-wire(+) transmission.
    Weak to noise,
    Short distance transmission.
    Low cost
Term-1
Term-2
balanced
ground
signal(+)
signal(-)
ground
Term-1
Term-2
unbalanced
ground
signal
ground

## Slide 130: Type of Serial Communication
Transmission timing
  Synchronous
    Use a separate clock line to synchronize the data transmission.
    High speed transmission with high cost.
  Asynchronous
    Self-timed transmission by data lines.
    Sampling & detecting using internal timing generator.
    Low speed transmission with low cost.
Term-1
Term-2
Synchronous
Data
Clock
Term-1
Term-2
Asynchronous
Data (self-timing)
Timing generator

## Slide 131: Type of Serial Communication
Flow control
  The way of handshaking between transmitter & receiver.
Hardware flow control
  Dedicated control lines for flow control : RTS/CTS, DTR/DSR
  RTS (request to send)/CTS(clear to send) : The DTE asserts RTS to indicate a desire to transmit to the DCE, and in response the DCE asserts CTS to grant permission.
  DTR (data terminal ready)/DSR(data set ready) : to indicate that the terminal is ready for communications and the modem may initiate a communications channel. DSR is set when DCE is ready to receive and send data.

## Slide 132: Type of Serial Communication
Software flow control
  Flow control by software
    Control the flow control using control characters(XON/XOFF code).
      Xmodem

## Slide 133: USART
USART(Universal Sync/Async Receiver/Transmitter)
  Typical serial communication protocol
    Serial port, COM port, RS-232C.
Frame format of USART packet
  Start bit : Indicate the transmission is started. Logical low.
  Stop bit : Indicates the transmission is finished. Logical high.
  Data bit : data bit
  Parity-bit : bit for parity checking

## Slide 134: USART
Physical interface(line driver/receiver) is required for long-distance transmission.
  Standard physical interface
    RS-232C (EIA), V.24 (CCITT), ISO 2110 (ISO)
    RS-423, RS-422, RS-485
http://mirine35.egloos.com/viewer/5057212
Tx
Rx
Tx
Rx
GND
GND
Line driver/receiver
TTL level

## Slide 135: USART
Comparison of physical interfaces
http://arindamcctvaccesscontrol.blogspot.com/2015/03/rs422-rs485-comparison-with-rs232.html
Single-ended : unbalanced. 2-wire(Tx, Rx). common GND.
Differential : balanced. 4-wire(Tx+, Tx-, Rx+, Rx-).

## Slide 136: USART
Serial connectors and signal connections
인용 : http://mirine35.egloos.com/viewer/5057212

## Slide 137: USART
Serial ports of Windows PC
  COM1,2,3,4
  Virual COM : simulation of serial port using USB port
  Serial monitor program
    Monitoring the data to transmit/receive to/from serial port.
      Data transmit : keyboard
      Data received : display on screen.
    hyperterminal

## Slide 138: Serial Port of ATmega328
USART
  1 ports
    2-wire Sync/Async
SPI
  1 port
    3-wire Sync
TWI (Two-wire Serial Interface)
  1 port
    2-wire Sync
    Same as Philips I2C

## Slide 139: ATmega2560 USART
1 x USART port
  USART0
Features
  Full Duplex Operation (Independent Serial Receive and Transmit Registers)
  Asynchronous or Synchronous Operation (Master or Slave Clocked Synchronous Operation)
  Supports Serial Frames with 5, 6, 7, 8, or 9 Data Bits and 1 or 2 Stop Bits
  Odd or Even Parity Generation and Parity Check Supported by Hardware
  Data OverRun/Framing Error Detection
  Noise Filtering Includes False Start Bit Detection and Digital Low Pass Filter
  Three Separate Interrupts on TX Complete, TX Data Register Empty and RX Complete
  Multi-processor Communication Mode
  Double Speed Asynchronous Communication Mode

## Slide 140: Block Diagram of USART

## Slide 141: Clock Generator
Provides clock to transmitter and receiver
  Clock source : internal clock or external clock
  baud rate generator
    Consists of UBRR (USART Baud Rate Register) & down counter.
Sync / Async ?
Double / Normal ?
Internal / External ?
Rising / Falling ?

## Slide 142: Clock Generator
The USART supports four modes of clock operation
  Normal asynchronous, Double Speed asynchronous, Master synchronous and Slave synchronous mode.
  The UMSELn bit in USART Control and Status Register C (UCSRnC) selects between asynchronous and synchronous operation.
  Double Speed (asynchronous mode only) is controlled by the U2Xn found in the UCSRnA Register.
  When using synchronous mode (UMSELn = 1), the Data Direction Register for the XCKn pin (DDR_XCKn) controls whether the clock source is internal (Master mode) or external (Slave mode).
    The XCKn pin is only active when using synchronous mode.

## Slide 143: Internal Clock Source
Reference clock for baud rate generator is generated by internal system clock.
  Internal clock generation is used for the asynchronous and the synchronous master modes of operation.
The USART Baud Rate Register (UBRRn) and the down-counter connected to it function as a programmable prescaler or baud rate generator.
  The down-counter, running at system clock (fosc), is loaded with the UBRRn value each time the counter has counted down to zero or when the UBRRnL Register is written.
Frequency of baud rate generator’s clock output = fosc/(UBRR+1)

## Slide 144: Baud Rate Setting Table
When internal clock source is used, UBRR should be properly set according setting table.

## Slide 145: External Clock Source
User the external clock provided by XCK pin as the reference clock
  Use for synchronous slave mode.
  Clock detection by synchronization register & edge detector with 2 CPU clock delay.
  Max. frequency of external clock : < (fosc/4)
Synchronous Mode XCKn Timing
Data changed

## Slide 146: Frame Format
1 start bit
5,6,7,8,9 data bits
No, even, odd parity bits for error checking
1 or 2 stop bits

## Slide 147: USART Registers
UDR (USART I/O Data Register)
  Store transmit/receive data.
UCSRA/B/C (USART Control and Status Register A/B/C)
  Store control & status information.
UBRR (USART Baud Rate Register)
  Consist of UBRRH & UBRRL.
  Use for configuration of Baud rate.

## Slide 148: UDR
USARTn I/O Data Register (UDRn)
  The USART Transmit Data Buffer Register and USART Receive Data Buffer Registers share the same I/O address referred to as USART Data Register or UDRn.
  The receive buffer consists of a two level FIFO.

## Slide 149: UCSRA
USART Control and Status Register A (UCSRnA)
  RXCn : USART Receive Complete
  TXCn : USART Transmit Complete
  UDREn : USART Data Register Empty
  FEn : Frame Error
  DORn : Data Overrun
  UPEn : Parity Error
  U2Xn : Double USART Transmission Speed
  MPCMn : Multi-processor Communication Mode

## Slide 150: UCSRB
USART Control and Status Register B (UCSRnB)
  RXCIEn : RX Complete Interrupt Enable
  TXCIEn : TX Complete Interrupt Enable
  UDRIEn : USART Data Register Empty Interrupt Enable
  RXENn : Receiver Enable
  TXENn : Transmitter Enable
  UCSZn2 : Character Size
  RXB8n : Receive Data Bit 8
  TXB8n : Transmit Data Bit 8

## Slide 151: UCSRC
USART Control and Status Register C (UCSRnC)
  UMSELn : USART Mode Select, 0=async, 1=sync
  UPMn1:0 : Parity Mode, 00=disabled, 10=even, 11=odd
  USBSn : Stop Bit Select, 0=1-bit, 1=2-bit
  UCSZn : Character Size, 000=5-bit, 001=6-bit, 010=7-bit, 011=8-bit, 111=9-bit
  UCPOLn : Clock Polarity, 0=rising, 1=falling

## Slide 152: UCSRC
USART Control and Status Register C (UCSRnC)
  UMSELn : USART Mode Select, 0=async, 1=sync
  UPMn1:0 : Parity Mode, 00=disabled, 10=even, 11=odd
  USBSn : Stop Bit Select, 0=1-bit, 1=2-bit
  UCSZn : Character Size, 000=5-bit, 001=6-bit, 010=7-bit, 011=8-bit, 111=9-bit
  UCPOLn : Clock Polarity, 0=rising, 1=falling

## Slide 153: UBRR

## Slide 154: Procedure of USART Initialization
Set the baud rate using UBRR.
Select frame format using UCSRC.
Enable transmitter/receiver UCSRB.
Set global interrupt mask & USART interrupt mask.

## Slide 155: Procedure of Data Transmitting/Receiving
Data transmission
  Activate the transmitter by setting TXEN(transmit enable) flag of TUCSRB register to ‘1’.
  If data is written to UDR, the transmission starts.
    In case of 9-bit data transmission mode, TXB8 bit of UCSRB register should be written before transmission starts.
  After the transmission is completed, UDRE(data register empty) flag becomes ‘1’.
Data Receiving
  Ready to receive if the RXEN(Receive Enable) flag of USRB register set to ‘1’.
  If valid start bit is detected, data receiving is started, and stop if stop bit is detected.
  After receiving is ended, RX flag becomes to ’1’.
    In case of 9-bit data reception mode, RXB8 bit of UCSRB register should be read before UDR is accessed.

## Slide 156: Data Sample Timing
Data sampling speed
  Normal mode : 16 * baud rate
  Double speed mode : 8 * baud rate
Decision of value
  By majority voting
    If more than 2 among 3 samples have same value, that value is the value of sample.

## Slide 157: Data Sample Timing
If high-to-low transition occurs before stop-bit finished, it becomes a start bit.
Early start bit detection
Ending point of stop bit
In normal mode, this transition is thought as start bit.
In double speed mode, this point as start bit

## Slide 158: Multi-processor Communication Mode
Multiple CPU can connect to each other through one serial bus.
  The type of data frame is categorized into pure data frame & address frame.
    Address frame contains address information to identify target transceiver.
Setting the Multi-processor Communication mode (MPCM) bit in UCSRnA enables a filtering function of incoming frames received by the USART Receiver.
  Frames that do not contain address information will be ignored and not put into the receive buffer.
Frame type bit
  Identify whether the current frame is data frame or address frame.
    ‘0’ (data frame), ‘1’ (address frame)
  When the size of data is 5~8 bits, the first stop bit is frame type bit.
  For 9-bit data, RXB8(9th bit) is frame type bit

## Slide 159: Multi-processor Communication Mode
Communication procedure
  All Slave MCUs are in Multi-processor Communication mode (MPCMn in UCSRnA is set).
  The Master MCU sends an address frame
  All slaves receive and read this frame. In the Slave MCUs, the RXCn Flag in UCSRnA will be set as normal.
  Each Slave MCU reads the UDRn Register and determines if it has been selected. If so, it clears the MPCMn bit in UCSRnA, otherwise it waits for the next address byte and keeps the MPCMn setting.
  The addressed MCU will receive all data frames until a new address frame is received. The other Slave MCUs, which still have the MPCMn bit set, will ignore the data frames.
  When the last data frame is received by the addressed MCU, the addressed MCU sets the MPCMn bit and waits for a new address frame from master. The process then repeats from 2.

## Slide 160: USART Circuit Example

## Slide 161: USART Source Code Example
#include<avr/io.h>
void putch(unsigned char data) {
while((UCSR0A & 0x20) == 0); // wait till UDRE0 = 1
UDR0 = data;
UCSR0A |= 0x20; // clear UDRE0
}
int main(){
unsigned char text[] = “hello”;
unsigned char i=0;
DDRE = 0xfe;
UCSR0A = 0x00; // MPCM = 0
UCSR0B = 0x18; // TXEN, RXEN = enable
UCSR0C = 0x06; // Async, No parity, 1 Stop, 8 data
UBRR0H = 0x00;
UBRR0L = 0x03; // 115200 bps @ 7.3728M
while(text[i] != ‘\0’) putch(text[i++]);
return 0;
}

## Slide 162: Q & A